Physical Tests

- Physical analysis of a stream is based on the following tests

  - Depth

  - Velocity

  - Volume of Flow/Stream Flow

  - Temperature

  - Turbidity

Depth (m):

- Depth is needed to calculate Volume of Flow

- Calculation:

  - Measure the width of the stream profile

  - Measure the depth at 1-meter intervals across the stream profile

  - Calculate the sum of all depth measurements

  - Divide the sum of depths by the number of measurements

* At most points in the Brandywine that we test, the depth will be less then 1 meter but the measurement should always be recorded in meters not centimeters

Velocity (m/sec):

- Velocity is a measure of how fast the stream water is moving

- Calculation

  - Measure the width of the stream profile

  - Divide the width by 5 – you will take measurements at 4 points (not on the very edge of the stream)

  - Velocity is measured by timing the movement of a tennis ball over 1 meter

  - Record three sets of times for each point across the river and take the average

  - Calculate the sum of the 4 averages and divide by 4 to get an overall average velocity

Volume of Flow/Stream Flow (m3/sec):

- The volume of water that moves past a fixed point in a specific interval of time

- Stream flow or volume of flow is an important indicator of water quality.

  - Affects the available oxygen level in water that fish and other aquatic wildlife depend on to live.

    - Streams with higher flows have more oxygen available for aquatic wildlife.

  - Controls the amount of sediment that is transported in a stream.

  - Determines how pollution is transported and influences the ability of a stream to dilute pollution.

    - Large, swift rivers have a greater ability to dilute and degrade runoff pollutants, unlike smaller streams.

- Calculation:

  - (width) x (average depth) x (average velocity) x (bottom constant)

    - Bottom Constant =

      - 0.8 if bottom is rough: rocks and course gravel

      - 0.9 if bottom is smooth: mud, sand, or bedrock

Water Temperature (°C):

- Temperature of the water directly affects biological and chemical processes.

  - Lower Temperature ( More Dissolved Gases (DO)

- Determines the type and location of organisms

  - Some fish species prefer colder waters than other species.

  - Bottom dwelling organisms will move in the stream in order to find their optimal temperature.

- Calculation:

  - Temperature is measured at 4 points throughout the stream profile

  - Divide the sum of the measurements by 4 to get the average

Turbidity

- Turbidity is a measure of water clarity.

- Insoluble solids or suspended particles such as clay, silt, sand, algae, plankton and other substances affect the clarity of the water.

- Water temperature is increased because suspended particles absorb more heat.

- When turbidity is high, photosynthesis is reduced due to the decrease in the amount of light traveling through the water.

- Sources of turbidity include

  - soil erosion

  - waste discharge

  - urban runoff

  - eroding stream banks

  - large numbers of bottom feeders that stir up sediments

  - excessive algal growth

- Measured using a Turbidity Tube

- Unpolluted Streams: >53.4 cm